## Slide 1
ERC confirmation
Date : Jul.28.2016
Name : TamDo
Department/Group/Team : Backend/Backend3/IO

## Slide 2: 1. Lacking power/ground connection for PSW cell.
Power switch is not connect to Power/Ground as IP level. It will be connected at TOP by upper layer.
 We should virtual connect it by using text.lis file.
M10 power pin of PSW is not connected to PG mesh
M10 core mesh
M10 core mesh
M10 core mesh
M10 core mesh
M10 core mesh
From LVS report:
X4743/X30530/M0(-4458.283,1886.477) MP(pch_svt_mac) ** unmatched instance **
X4743/X30530/M1(-4458.283,1885.421) MP(pch_svt_mac) ** unmatched instance **
…
** unmatched instance ** FSACA9SB0YSRSBSMAW120R12/MM0==199 MP(pch_svt_mac)
** unmatched instance ** FSACA9SB0YSRSBSMAW120R12/MM0==200 MP(pch_svt_mac)
It means that layout and netlist has these device, but it does not same connection when LVS compare
Solution. We set virtual connection for these line
LAYOUT TEXT "VDDM_A2VC1" -5204.880 2195.573 140 "u7795hrcah30vcd0_a2vc1_PV“
LAYOUT TEXT "VDD" -5204.880 2193.075 140 "u7795hrcah30vcd0_a2vc1_PV"

## Slide 3: 2. Short signal
Short signal which is defined in text.lis file
From LVS report
NUMBERS OF OBJECTS AFTER TRANSFORMATION
---------------------------------------
Layout Source Component Type
------ ------ --------------
Ports: 10322 10325 *
Nets: 561775 561780 *
…
**************************************************************************************************************
INCORRECT NETS
DISC# LAYOUT NAME SOURCE NAME
**************************************************************************************************************
1 ** missing net ** u_BRIDGE_u_adb400_r_payld_async[572]
--------------------------------------------------------------------------------------------------------------
2 ** missing net ** u_BRIDGE_u_adb400_r_payld_async[856]
--------------------------------------------------------------------------------------------------------------
3 ** missing net ** u_BRIDGE_u_adb400_cd_payld_async[660]
--------------------------------------------------------------------------------------------------------------
4 ** missing net ** u_BRIDGE_u_adb400_w_payld_async__489__OUT_PORT_BUF_net
--------------------------------------------------------------------------------------------------------------
5 ** missing net ** u_BRIDGE_u_adb400_w_payld_async__374__OUT_PORT_BUF_net
--------------------------------------------------------------------------------------------------------------
These net connected to port of IP. These port already defined in text.lis file
 LVS can export the lvs.rep.short file
LAYOUT TEXT "u_BRIDGE_u_adb400_cd_payld_async[660]" 755.89 -309.1 132 u7797hca53ss0_pva2ls_PV
LAYOUT TEXT "u_BRIDGE_u_adb400_cd_payld_async[572]" 755.89 -467.3 132 u7797hca53ss0_pva2ls_PV
LAYOUT TEXT "u_BRIDGE_u_adb400_cd_payld_async[856]" 755.89 -479.4 132 u7797hca53ss0_pva2ls_PV
To easy detect short, we should define net name into text.lis file

## Slide 4: 3. Short signal
Using Hcell to find properly short location
LVS report without define DCAP4BWP7T40P140 in Hcell  200 instance were reported (maximum)  hard to find short location
Error: Different numbers of nets.
Error: Connectivity errors.
**************************************************************************************************************
INCORRECT NETS
DISC# LAYOUT NAME SOURCE NAME
**************************************************************************************************************
1 Net X272/X16317/6 Xxofiller_CAP_DCAP4BWP7T40P140_23035/net044
--- 3 Connections On This Net --- --- 3 Connections On This Net ---
-------------------------- --------------------------
--- Incorrect Devices On This Net ---
X272/X16317/X0/M1(-1865.240,1333.275) MP(pch_mac) Xxofiller_CAP_DCAP4BWP7T40P140_161727/MM27 MP(pch_mac)
s: VDD s: VDD
d: VDD d: VDD
b: VDD b: VDD
g: X272/X16317/6 ** Xxofiller_CAP_DCAP4BWP7T40P140_23035/net044 **
** X326/X56776/6 ** g: Xxofiller_CAP_DCAP4BWP7T40P140_161727/net044
…
200 Net X272/X17381/6 Xxofiller_CAP_DCAP4BWP7T40P140_23535/net044
--- 3 Connections On This Net --- --- 3 Connections On This Net ---
-------------------------- --------------------------
--- Incorrect Devices On This Net ---
X272/X17381/X1/M1(-1781.100,1333.275) MP(pch_mac) Xxofiller_CAP_DCAP4BWP7T40P140_23061/MM27 MP(pch_mac)
s: VDD s: VDD
d: VDD d: VDD
b: VDD b: VDD
g: X272/X17381/6 ** Xxofiller_CAP_DCAP4BWP7T40P140_23535/net044 **
** X272/X16330/6 ** g: Xxofiller_CAP_DCAP4BWP7T40P140_23061/net044
 We can guess there are short between internal wire of DCAP and signal.
LVS report after define DCAP4BWP7T40P140 in Hcell  Only 1 DCAP cell reported  short location.
Error: Cells with non-floating extra pins.
*******************************************************************************************
INSTANCES OF CELLS WITH NON-FLOATING EXTRA PINS
DISC# LAYOUT NAME SOURCE NAME
*******************************************************************************************
1 X284/X44462/X1(-1933.260,660.880) DCAP4BWP7T40P140 Xxofiller_CAP_DCAP4BWP7T40P140_91620 DCAP4BWP7T40P140
X284/X44462/X1/1:X284/46908 ** missing pin ** Xxofiller_CAP_DCAP4BWP7T40P140_91620/net044 ?
To easy detect short, we should define cell name into Hcell file

## Slide 5: 4. MISSING PIN at IP level
LVS report
------
Error: Connectivity errors.
Error: Cells with non-floating extra pins.
…
DISC# LAYOUT NAME SOURCE NAME
**************************************************************************************************************
1 X102/X0(-1833.245,-3570.710) u7797hrcav3mmm00 Xmm u7797hrcav3mmm00
X102/X0/2:VDDQ_MDPLL0 ** missing pin ** ? VDDQ_MDPLL0
X102/X0/3:VDDQ_MAPLL ** missing pin ** ? VDDQ_MAPLL
X102/X0/5:VDDQ_MDPLL1 ** missing pin ** ? VDDQ_MDPLL1
------
This error is caused by using wrong FRAM. FRAM of MM is missing PORT VDDQ_MDPLL0, VDDQ_MDPLL0, VDDQ_MDPLL0
So, The PG connect is not effected.

## Slide 6: 4. LVS INCORRECT at STD/DCAP cell
Using Hcell to find properly short location
LVS report
------
Error: Cells with non-floating extra pins.
…
INCORRECT AN3D0BWP7D5T24P96CPD AN3D0BWP7D5T24P96CPD
…
------
In correct at std-cell can judge by:
--- lacking PG connect for these cell
--- short signal caused incorrect PIN

## Slide 7: 5. LVS INCORRECT at CAP/BOUND cell
Hcell: collection of extracted cells in layout design
Lacking of CAP/BOUND cells: not remove placement blockage? Gdsmerge exists any error?
**************************************************************************************************************
INCORRECT INSTANCES
DISC# LAYOUT NAME SOURCE NAME
**************************************************************************************************************
1 ** missing instance ** Xboundarycell_ENDCAP_TSHFILL20T_153503__PUSHDOWN TSHFILL20T
--------------------------------------------------------------------------------------------------------------
2 ** missing instance ** Xboundarycell_ENDCAP_TSHFILL20T_153504__PUSHDOWN TSHFILL20T
--------------------------------------------------------------------------------------------------------------
3 ** missing instance ** Xboundarycell_ENDCAP_TSHFILL20T_153533__PUSHDOWN TSHFILL20T

## Slide 8
Renesas System Design Co., Ltd.