## Slide 1
Blockage & GuardRing
  Naming Rule
2022/8/3
Y.Mori
ABDD/ABB12
ルネサス エレクトロニクス株式会社

## Slide 2
Appendix
・Blockage naming rule
・Guard ring naming rule
・Guard ring distance rule
SHDB setting
Restore SHDB
Create Floor Plan
Check Floor Plan
Die Setting
Pre check
Guar Ring Overlap
Create non default Row
Guar Ring Cell insertion
Create Power Domain
Check Row align
Insert
EndCap & Tap Cell
Check Fplan
Place EPD Cell
Definition
Custom(P/G) Route
Initial Setting
Additional User Setting
Custom STA Setting
Save database
floor plan flow (100_init.tcl)
This document describes this part.
Make core7T Row Area
Cut core7T Row
IO Place
Generate Track
Place Hard Macro
Read UPF
Set Blockage for Non default Row
Check Blockage coordinate
This document describes the procedure for creating Row, Voltage Area and Guard Ring using INNOVUS.
Scope of description in this document
Create Guard Ring blockage
Insert
TDC dummy cell
5V Level Shifter place
core107T,core79TD

## Slide 3: Image of row creation procedure
Floor plan designs using INNOVUS utilize shapes drawn using placement blocks.
Row and voltage area are created based on blockage data.
Please complete the design of IO placement and HM place in advance.

## Slide 4: Image of the scope of this document
IO.def
HM_place.def( or Tcl)
Scope of description in
this document
How to create Row and
inserted guardring and
end/tap cell ?
Create core7T Row
Cut Row(core7T)
Create Row(core48T/core79TD/core107)
Create Voltage Area
Insert End Cap / Tap Cell
Place Guard Ring Cell
It does not mention the procedure of IO placement and macro placement.
die
Floor Plan

## Slide 5: Image of row creation procedure
Fill core7T
Cut out row under the
placement blockage
Create other core rows
Make Blockage shape for create core48T
Make Blockage shape for create core79TD
Make Blockage shape for create core107T
Make Blockage shape for nondefault
Voltage area on core7T
Make Placement Blockage shape for cut core7T
(Make by manual)
(Make by manual)
Make 4 type Blockage shape

## Slide 6: Image of Voltage Area creation procedure
Row position expressed by blockage shapes.
Create a Voltage Area by referring to the blockage shape and blockage attribute.
utility
Core48 blockage shapes
core7 blockage shapes
(non default Domain)
Core79 blockage shapes
Core107 blockage shapes
Generate Voltage Area

## Slide 7: Image of Insert End Cap / TapcelL procedure
End Cap and Tap cell are inserted using the INNOVUS native command.
Native CMD
After the create Row and Voltage Area
have been designed…
Place End Cap and Tap Cells.

## Slide 8: Image of Insert Guard Ring Cell procedure
Guard Ring cell is automatically inserted based on the placement blockage shape.
Utility
Guard Ring Cell
Singl Ring
Double Ring

## Slide 9: Scripts to help create floor plans
/design04/u2c8be1/data/u2c8/5_layout/50_PnR/501_INNOVUS/COMMON_INNO_7T
~/UTIL/util_create_core_box_and_row_for_u2c.tcl
~/UTIL/util_set_row_pd_island_for_u2c_v013a.tcl
~/UTIL/util_inn_check_misaligned_row.tcl
~/UTIL/util_regen_tracks_for_u2c.tcl
~/UTIL/NIMH.command.v4.1.etf
~/UTIL/util_change_row_for_moving_const_box_v003.tcl
~/UTIL/util_create_top_guardring_const_box.tcl
~/UTIL/util_insert_TCD_dummy.tcl
~/UTIL/utl_check_narrow_placement_space_v2.etf
~/UTIL/utl_check_tech_site_and_library_cell_site_in_PD_v2.etf
~/UTIL/util_check_pg_diff.tcl
~/UTIL/util_dump_phycell_prefix_v001.tcl
~/CMD/endcap_tap_insertion_NIMHR_site_v007.tcl
~/CMD/endcap_tap_insertion_default_site_v006.tcl
~/CMD/check_fplan_for_u2c_v007.tcl
~/UTIL/util_CutRow_around_SoftBlkg.tcl
We have utilities to help you create floorplans.

## Slide 10: Die Size Definition
detailed Design

## Slide 11: Die size definition
There are rules for Die size dimensions.
X size must be an integral multiple of the standard Row site.
Y size must be an integral multiple of the standard Row height.
Die
In the IO.def definition…
DIEAREA ( -6475000 -5716200 ) ( 6475000 5716200 ) ;
0.7um x 2n
0.14um x 2n
core7T height
core7T site
Row Hight x 2n
Row unit x 2n
X (0,0)
X (0,0)
NG
OK
In Innovus, Placement Grid is made
based on the lower left corner of the chip.
Std cell is placed at the row site.
If there is a gap in the coordinate,
a large number of grid errors will occur
when the placement check is performed.
Die size must be designed so that the Placement Grid and the Row site match.
Die size

## Slide 12: Die size definition
#### 2.1 shiftOrigin ####
shiftOrigin -center
#### 2.2 io place ####
defin $IO_def
# IO Y flip request from ABB13. 2022/7/26
source /design04/u2c8be2/u2c8/data/u2c8/6_layoutchk/MASTER_PG/06_IO/IO_SOSC_upper_flip.tcl
#### 2.3 HM place ####
defIn $HM_def
deleteHaloFromBlock -allIOPad
deleteHaloFromBlock -allBlock
100_init.tcl
HM.def
HM_place.def( or Tcl)
It does not mention the procedure of IO placement and macro placement.
The IO.def will be provided by physics design team.
The chip size is set to INNOVUS to the value described
in DIEAREA of DEF.
IO.def
Consider the placement of HM in advance
and keep the placement information.

## Slide 13: UPF Setting
detailed Design

## Slide 14: READ UPF
#### 2.6 read upf ####
source -e -v $mask_list_upf ; # Variable Settings For Reading UPF File Correctly
read_power_intent -1801 ${upf_file}
commit_power_intent -keepRows -power_domain
***worst.upf + ***worst_srsn.tcl (cat)
Merged into one file
Variable settings defined in UPF（If necessary)
Merge the master UPF and subfiles into one file.
If you want to change the UPF during design,
Execute the above command repeatedly.
Power assign will be changed to the new setting.

## Slide 15: Row creation procedure
detailed Design

## Slide 16: Make Blockage shape for cut core7T
Full core7T
X {0 0}
Cut core7T Row
### 2.4 resette core box and base row ####
deleteRow -all
util_create_core_box_and_row_for_u2c
createPlaceBlockage -type hard -box {0 0 10 10} -name origin
100_init.tcl
X {0 0}
util
Die
{0 0｝
+
Generates a core7T row for the whole chip.
core7T Row
core7T Row
Use this mark to check if the origin position is correct.
put origin marker

## Slide 17: Make Blockage shape for cut core7T
Create placement blockage that removes areas where the core7T is not needed.
Cut core7T Row
IO
AD area
SYS area
AWO area
ISO area
PHY
5V repater
5V area
core7T area
IO
ISO area
Consider a floor plan
Create a blockage that
covers areas other than
the Core7T area
Cut core7T row area
Placement blockage file
Dump to placement blockage file

## Slide 18: Make Blockage shape for cut core7T
Full core7T
Cut unnecessary rows
There are naming rules for blockage shapes.
createPlaceBlockage -type partial -density 50 -name For_Cut_row_pb -box {-1477.840 2155.300 -777.140 2566.900}
createPlaceBlockage -type partial -density 50 -name For_Cut_row_pb -box {1820.140 2127.300 1894.200 2566.900}
createPlaceBlockage -type partial -density 50 -name For_Cut_row_pb -box {2459.940 2114.700 2905.900 2179.100}
:
:
①
②
①：-type can be decided arbitrary.
②：-name should be “For_Cut_Row_pb*”
Cut Row under the Placement Blockage.
X {0 0}
In 100_init.tcl, the cut row is executed with this name.
Be sure to give “For_Cut_Row_pb*” to blockage
name.
Cut core7T Row

## Slide 19: Make Blockage shape for cut core7T
createPlaceBlockage -type partial -density 50 -name For_Cut_row_pb -box {-1477.840 2155.300 -777.140 2566.900}
createPlaceBlockage -type partial -density 50 -name For_Cut_row_pb -box {1820.140 2127.300 1894.200 2566.900}
createPlaceBlockage -type partial -density 50 -name For_Cut_row_pb -box {2459.940 2114.700 2905.900 2179.100}
:
:
Corresponding part in the 100_init.tcl
Cut Row under the Placement Blockage.
:##### 2.7 create core7T Row ####
source $pKl_for_CutRow_core7T
set cutRow_area [dbShape [dbGet top.fPlan.pBlkgs.boxes]]
foreach i $cutRow_area {
cutRow -site core7T -area $i
}
cutRow -halo 0.14
Content
Cut Row under the Hard Macro sets halo 0.14 to avoid DRV.
Space is required around the HM.
Row
100_init.tcl
Cut core7T Row
HM

## Slide 20: Create non default Row procedure
core48T, cre79TD core107T

## Slide 21: Make Blockage shape for except core7T row
core107
core79
core48
Non default voltage core7 area
Multi-height Row and Voltage areas are generated based on the shape expressed by the blockage.
Blockage file
Make Blockage shape for except core7T row
Set Blockage for Non default Row
Work manually.

## Slide 22: Create non default Row procedure
Non default Row are created by referring to the blockage shape and blockage attribute.
Innovus > util_set_row_pd_island_for_u2c -job_type row
P12~P16
Guar Ring Cell insertion
Use the utility to create Row.
core48 blockage shape
core79 blockage shape
core107 blockage shape

## Slide 23: Make Blockage shape for create core48T
Only core7T rows
Add core48T rows
Make a Placement Blockage for create core48T row.
The blockage shapes expresses where you want
to make the core48T.
Core48T row and voltage area creation and Guard
Ring cell are automatically generate based on this
created placement blockage attribute.
createPlaceBlockage -type hard -name core48T%PD_SYSVCC_VSS%5V%woDNW -box { …}
createPlaceBlockage -type hard -name core48T%PD_VCC_VSS%5V%woDNW -box { …}
createPlaceBlockage -type hard -name core48T%PD_A1VCC_A1VSS%5V%wDNW -box { …}
:
:
①
②
①： The blockage type for generating the core48T
area is hard
②：Naming rules are strictly defined. see the
“Blockage Naming Rule for row Generation”
page for more information.
➂： The coordinates are required to be aligned with
the core47T placement grid.
There are naming rules for blockage.
➂
Point: To make core 48T, set type to hard.
blockage shape
Set Blockage for Non default Row

## Slide 24: Make Blockage shape for create core79TD
Make a Placement Blockage for create core79TD row.
The blockage shapes expresses where you want
to make the core79TDT.
Core79TD row, voltage area creation, and Guard Ring
Cell place are automatically generate based on this
Created placement blockage attribute.
createPlaceBlockage -type soft -name core79TD%PD_AWOVDD_VSS%E0VCC%VSS%1V%woDNW -box { …}
createPlaceBlockage -type soft -name core79TD%PD_PLLVDD_PLLVSS%AWOVDD%VSS%1V%woDNW -box { …}
createPlaceBlockage -type soft -name core79TD%PD_ISOVDD_VSS%A1VCC%A1VSS%1V%woDNW -box { …}
:
:
①
②
①： The blockage type for generating the core79TD
area is soft
②：Naming rules are strictly defined. see the
“Blockage Naming Rule for row Generation”
page for more information.
➂： The coordinates are required to be aligned with
the core79TD placement grid.
There are naming rules for blockage.
➂
Point: To make core 79TD, set type to soft.
Add core79TD rows
blockage shape
Set Blockage for Non default Row

## Slide 25: Make Blockage shape for create core107T
createPlaceBlockage -type macroOnly -name core107T%PD_A1VCC_A1VSS%ISOVDD%VSS%V5%woDNW%UL% -box {}
createPlaceBlockage -type macroOnly -name core107T%PD_E0VCC_VSS%ISOVDD%VSS%V5%woDNW%UL% -box { …}
createPlaceBlockage -type macroOnly -name core107T%PD_SYSVCC_VSS%AWOVDD%VSS%V5%woDNW%UL% -box {}
:
:
①
②
①： The blockage type for generating the core107T
area is macroOnly
②：Naming rules are strictly defined. see the
“Blockage Naming Rule for row Generation”
page for more information.
➂： The coordinates are required to be aligned with
the core107T placement grid.
There are naming rules for blockage.
➂
Add core107T rows
Make a Placement Blockage for create core107T row.
The blockage shapes expresses where you want
to make the core107T.
Core107T row, voltage area creation, and Guard Ring
Cell place are automatically generate based on this
Created placement blockage attribute.
Point: To make core 107T, set type to macroOnly.
blockage shape
Set Blockage for Non default Row

## Slide 26: Make Blockage shape for nondefault Voltage area on core7T
Put on non def voltage shape
Make a Placement Blockage for create nondefault
Voltage area on core7T.
Non default voltage area creation and Guard Ring
Cell place are automatically execute based on this
Created placement blockage attribute.
createPlaceBlockage -type partial -density 10 -name core7T%PD_AWOVDD_VSS%1V%woDNW -box {…}
createPlaceBlockage -type partial -density 10 -name core7T%PD_PLLVDD_PLLVSS%1V%wDNW -box { …}
createPlaceBlockage -type partial -density 10 -name core7T%PD_HOCOVDD_VSS%1V%woDNW-box {}
:
:
①
②
①：The blockage type for generating the non default
area is partial (density value is arbitrary)
②：Naming rules are strict. see the
“Blockage Naming Rule for row Generation”
page for more information.
➂： The coordinates are required to be aligned with
the core7T placement grid.
There are naming rules for blockage.
➂
Point: To define VA on core7T, set type to partial.
blockage shape
Set Blockage for Non default Row

## Slide 27: Create non default Row procedure
Innovus > util_set_row_pd_island_for_u2c -job_type row
Guar Ring Cell insertion
Note
This command can generate core7T row under blockage name core7T*.
but core7T row was existed in the first step.
It don't need to create the core7T in this phase.
(You will need this blockage file in a later process.)
Cut core7T Row
#### 2.11 create non default row area ####
deletePlaceBlockage core7T*
util_set_row_pd_island_for_u2c -job_type row
source $pKl_for_NonDefaultVA_core7T
100_init.tcl
In 100_init.tcl , delete core7T* before execute this command.
Then source the blockage file again.

## Slide 28: background knowledge
# reference(dummy) row creation ###
set rows {core7T core48T core79TD core107T}
set x1 [lindex [dbGet top.fplan.coreBox] 0 0]
set y1 [lindex [dbGet top.fplan.coreBox] 0 1]
set y2 [lindex [dbGet top.fplan.coreBox] 0 3]
set offset "0"
foreach i $rows {
cutRow -site core7T -area [expr $x1 + $offset] $y1 [expr $x1 + $offset + 20] $y2
createRow -site $i -area [expr $x1 + $offset] $y1 [expr $x1 + $offset + 20] $y2
set offset [expr $offset + 25]
}
100_init.tcl
Die
During the row generation process, create a dummy row
indicating the reference position at the left side of the chip.
Put dummy row
The row coordinate check is based on the referenced row.
After checking the coordinates of all Rows, it will be deleted because it is no longer needed.
core7T,core48T,core79TD,core107

## Slide 29: Guard Ring Insertion procedure

## Slide 30: Insert Guard Ring Cell procedure
There are three types of guard rings.
・IO Guard Ring Cell
・Row Guard Ring Cell
・Hard Macro Guard Ring Cell
IO guard ring
HM guard Ring
AD
IO guard Ring
Row
Row guard Ring
There is a utility that places the guard ring cell along the edge of the placement block.
At first, You need to prepare placement blockage file for the guard ring implementation.
１）Blockage for generate IO guard ring ; >> There is utility to create it .
２）Blockage for generate Row guard ring ; >> Use the blockage file for row creation.(don’t need re-make it)
３）Blockage for generate HM guard ring ; >> Must be made by hand.
*For Soft IP ( like Fusa) guard ring generate is
the almost same procedure as the Row guard
ring. See page 36 for details

## Slide 31: Insert Guard Ring Cell procedure
Guard Ring Cell insertion .
Pre check
Guar Ring Overlap
IO guard ring
AD
IO guard ring
AD
Utility
For IO
For Row
For HM
Blockage shape check
Step 1
Prepare the blockage
Step 2
Pre-check the overlap of
Guard ring cells using the
blockage shape.
Step 3
execute utility.
Image

## Slide 32: Insert Guard Ring Cell procedure
How to make Placement blockage for IO guard ring.
You can use the utility to create a template blockage file.
Innovus > util_create_top_guardring_const_box -multistage_row_gap 30.0 -offset 8.0
Use the utility to create a placement blockage.
Offset
gap
IO guard ring
Offset
gap
Utility
Blockage
Generate Blockage
Create Guard Ring blockage
21-5 RV28F_ラッチアップ対策チップ実装ガイド_V1.0.pptx
This is the guard ring insertion specification ＞＞
I/O
Blockage edge
G/R
G/R
I/O
Offset must be set
ESD LUP rule >10.0um
G/R Hight 2um
If generated blockage shape is not expected, you will need to modify the shape by manual.
And dump the blockage information.
Innovus > select_obj [dbGet top.fplan.pBlkgs.name top_guardring_const_box -p]
Innovus > writeFPlanScript -selected –filename mod_top_guardring_const_box.tcl
The recommended offset value is 8.0 or less.

## Slide 33: Insert Guard Ring Cell procedure
Create Guard Ring blockage
Blockage shapes for row generation
A guard ring is generated based on same files.
How to make Placement blockage for Row guard ring.
You can use the same blockage files as for Row generation.
So, you don't need remake blockage for row guard ring.
Row

## Slide 34: Insert Hard Macro Guard Ring Cell procedure
How to make Placement blockage for HM guard ring.
AD
AD
It is necessary to make a placement blockage shapes for the HM guard ring cell implementation.
Utility
This blockage also has a naming rule.
See the Naming Rules chapter in the appendix.
Blockage naming rule; HardIP%Power_Domain_name%%%5V%woDNW%<IP>%<Suffix>
Create Guard Ring blockage
AD

## Slide 35: Insert Hard Macro Guard Ring Cell procedure
Precautions for HM blockage generation
HM
Space> 5um
Space> 5um
G/R cell
specification
PB
Space=3.1um
Space=3.1um
The utility script is generated
guardring cells at a distance of
3.1um from the blockage edge.
G/R cell
HM
Space> 5um
Space> 5um
G/R cell
Edge from PB
3.1um
Edge from PB
3.1um
Offset 1.9um
Offset 1.9um
PB
You need to extend the
placement blockage.
We are considering a revision of the script.
Create Guard Ring blockage

## Slide 36: Insert Guard Ring Cell around Soft IP (Fusa)
Create Guard Ring blockage
.
Soft IP
(Fusa IP)
Cut Row
Place G/R
Blockage naming rule; SoftIP%Power_Domain_name%%%1V%woDNW%<IP>%<Suffix>
Make a placement blockage cover the target soft IP area
G/R Cell
3um
3um
Soft IP
Cut Row area by CutRow_around_SoftBlkg CMD.
Use the utility to cut the Row around the blockage.
Utiliy; CutRow_around_SoftBlkg
This command finds blockage with the name SoftIP* and cut row around it.
How to make Placement blockage for Soft IP guard ring.

## Slide 37: Insert Guard Ring Cell procedure
Innovus > util_set_row_pd_island_for_u2c -job_type check_all -gr_setting_file gr_setting_file.txt
You can pre-check guard ring cell overlap from each blockage shape using the command below.
Row blockage
IO guard Ring
Row guard Ring
IO cells
Such overlap can be detected from the pre-check.
Implementing the Guard ring insert takes about an hour.
By checking the overlap of guard rings cells in advance,
it is possible to prevent failures after cell insert.
Pre check
Guar Ring Overlap
Over lap
HM
Over lap
HM guard Ring
・Pre-check
Release with the utility.

## Slide 38: Insert Guard Ring Cell procedure
For IO Guard Ring cell insertion utility command.
Innovus > util_set_row_pd_island_for_u2c -job_type gr -gr_setting_file gr_setting_file.txt -sites top_guardring_const_box
Innovus > deletePlaceBlockage top_guardring_const_box*
For Row and HM and Soft IP guardring cell insertion utility command.
Innovus > util_set_row_pd_island_for_u2c -job_type gr -gr_setting_file gr_setting_file.txt
Release with the utility.
Inert Guard Ring
Guar Ring Cell insertion
Before insert row & HM guard Ring,
delete IO placement blockage.

## Slide 39: Insert Guard Ring Cell procedure
Guar Ring Cell insertion
### 2.9 create_IO_guardring_const_box ###
# util_create_top_guardring_const_box -multistage_row_gap 30.0 -offset 2.0
source $FP_Blockage/tmp_top_guardring_const_box_1113.tcl
#suspend
#### 2.10 Check Guard Ring Overlap ####
util_set_row_pd_island_for_u2c -job_type check_all -gr_setting_file $FP_data/gr_setting_file_v004.txt -out_file set_pd_site_info.tcl
#### 2.11 create non default row area ####
deletePlaceBlockage core7T*
util_set_row_pd_island_for_u2c -job_type row
###
source $pKl_for_NonDefaultVA_core7T
#### 2.12 Guard ring cell insertion ####
Puts "Start: Guard ring cell insertion"
report_resource -start GR_cell
deletePowerSwitch
util_set_row_pd_island_for_u2c -job_type gr -gr_setting_file $FP_data/gr_setting_file_v004.txt -sites top_guardring_const_box
deletePlaceBlockage top_guardring_const_box*
util_set_row_pd_island_for_u2c -job_type gr -gr_setting_file $FP_data/gr_setting_file_v004.txt
report_resource -end GR_cell
In the first step, execute this line to create a
reference blockage file.
Next step, read the edited reference blockage file.
100_init.tcl
Check the overlap of guard rings in advance.
Make creo48T,core79TD,creo107T Site Rows.
Restore the core7T blockage to generate a guard ring.
P30
P26
P38
P37

## Slide 40: Create power domain (voltage area) procedure

## Slide 41: Create Power domain (voltage area) procedure
Power domain are create by referring to the placement blockage shape and placement blockage attribute.
Innovus > util_set_row_pd_island_for_u2c -job_type pd -gr_setting_file gr_setting_file.txt
P18~P25
Use the utility to create voltage area.
core48 blockage shape
core79 blockage shape
core107 blockage shape
Create Power Domain
core7 non defolt blockage shape

## Slide 42: Create Power domain (voltage area) procedure
Create Power Domain
Note
There is a Power Domain whose elements are only HM.
Innovus > check_design -type {power_intent} -out_file ${rpt_dir}/check_design_power_intent.rep
Log;
---------------------------------------------------------------------------------------------------------------------------------
| ID | Severity | Count | Description |
---------------------------------------------------------------------------------------------------------------------------------
| IMPMSMV-8620 | error | 1 | Power domain (%s) has not given a legal fence. |
dict set design_checks power_intent IMPMSMV-8620 {
severity error
count 1
violations {
{PD_HSFD0RVCC_VSS}
}
}
check_design_power_intent.rep
HM
HM
PD_HSFD0RVCC_VSS
PD don't have a STD
In ICC2 , such a Power Domain does not make a Row and does not make Power Domain shapes.
But in INNOVUS it is an error.
Do the check to find such a power domain.
If there is an error
HM
HM
← Add PD_HSFD0RVCC_VSS Shape
FloorPlan
setObjFPlanBoxList Group $pd_name {boxlist}
setObjFPlanBoxList Group PD_HSFD0RVCC_VSS {2120.815 1969.94 2261.815 2037.94}

## Slide 43: Insert EndCap & TaPCell procedure

## Slide 44: Inert Endcap & tapcell procedure
Endcap & Tapcell are insert by referring to the placement blockage shape and placement blockage name.
# insert for non default site Row
Innovus > source $COMMON_INNO/CMD/endcap_tap_insertion_NIMHR_site.tcl
# insert for default site Row
Innovus > source $COMMON_INNO/CMD/endcap_tap_insertion_default_site.tcl
P18~P25
Use the utility to create voltage area.
No additional work is required.
Insert
EndCap & Tap Cell

## Slide 45: Check Fplan
Check Fplan
### ============================================================================
### --- check Fplan
### ============================================================================
Puts "Start: check Fplan"
set rpt_dir RPT
source $COMMON_INNO/CMD/check_fplan_for_u2c_v006.tcl
## SRAM Orientation check ##
source ${COMMON_INNO}/UTIL/safety_enable_macro_orientation_check_v7.tcl
read_macro_orientation_file -file ../../Top/U2C8_TCL/FP_data/check_tbl_RV28F_u2c8
check_macro_orientation -rule HM_chk_SPRAM_RV28F -summaryReport ${rpt_dir}/check_sum_sram_orientation_rule_HM_chk_SPRAM_RV28F.rep
check_macro_orientation -rule HM_chk_DPRAM_RV28F -summaryReport ${rpt_dir}/check_sum_sram_orientation_rule_HM_chk_DPRAM_RV28F.rep
## For Power domain check
check_design -type {power_intent} -out_file ${rpt_dir}/check_design_power_intent.rep
100_init.tcl
Check the floor plan you created using the script below.
~/RPT
checkFPlan_all.rep
checkPlace_*.rep
verify*
special_net_short_check.rep
~/RPT
check_design_power_intent.rep
In log file
Macro orientation check: PASSED
Macro orientation check: PASSED
* Checkpoint is discrived in chapter “Create Power Domain”
Output files
Output file

## Slide 46: Insert TCD dummy Cell
Insert
TDC dummy cell
TCD dummy cells are placed for 50% of the
2 mm x 2 mm compartments.
Example: Dummy placement is required in 13
sections, which is half of the 25 sections divided
by 2 mm x 2 mm.
Sections less than 2 mm square can be ignored.
（ Example: It is not necessary to insert DCT Cell
the A to K sections in the figure on the right. ）
2mm
2mm
①
②
③
④
⑤
⑥
⑦
⑧
⑨
⑩
⑪
⑫
⑬
⑭
⑮
⑯
⑰
⑱
⑲
⑳
㉑
㉒
㉓
㉔
㉕
A
B
C
D
E
F
G
H
I
J
K
TCD dummy cell placement specifications

## Slide 47: Insert TCD dummy
### ============================================================================
### --- TCD dummy cell place
### ============================================================================
Puts "Start: TCD dummy cell place"
set tcd_dummy_lef {BEOL_small_FDM1_20110323.lef BEOL_small_FDM2_20110323.lef BEOL_small_FDM3_20110323.lef BEOL_small_FDM4_20110323.lef BEOL_small_FDM5_20110323.lef}
foreach i $tcd_dummy_lef {
loadLefFile /eda01/Foundry2/TSMC/28HPL/Rules/DesignRule/LOGIC/v2.0/N28_TCD_library_kits_20110323/lef/BEOL_MX_4X/$i
}
if {[file exists $TCD_DUMMY_def]} {
defIn $TCD_DUMMY_def
} else {
util_insert_TCD_dummy -block_size 2000
util_insert_TCD_dummy -block_size 2000 -check
#saveDesign $db_dir/TCD_dummy_place.enc
}
Puts "End: TCD dummy cell place"
100_init.tcl
Insert
TDC dummy cell
Provides a utility that automatically finds no row area and places TCD Cells.
The automatically placed location is not always appropriate.
Please be sure to check.
i_BEOL_small_FDM1_2_0

## Slide 48: 5V Level Shifter place (core79TD,core107)
# 5V place(core107T,core79TD)
### COMMNET OUT. This is Guide for Level shifter placement.
### Temporarily comment out and therefore Innovus placer places LS to appropriate location.
### After above trial PnR , if we find wrong LS location, we will make new guide file for CN.
if { ${5V_flag} == "Y" } {
source ${COMMON_INNO}/UTIL/NIMH.command.v4.1.etf
setPlaceMode -place_global_exp_allow_missing_scan_chain true
enable_metric -off
placeInstsWithSites "core107T"
dbSet [dbGet top.insts.cell.site.name core107T -p3].pStatus fixed
placeInstsWithSites "core79TD"
dbSet [dbGet top.insts.cell.site.name core79TD -p3].pStatus fixed
enable_metric -on
saveDesign DBS/100_init_5V.enc
} else {
defIn ${5V_def}
}
100_init.tcl
INNOVUS cannot automatically place NIMH(Non Integer Multi Height) cells during PlaceOpt phase (200_place_opt).
( core79TD, core107T site cell =5V level down/Up shifter)
NIMH cell (5V Level shifter) is placed in the 100_init phase.
NIMH cells are placed using a “placeInstsWithSites” command.
5V Level Shifter place
core107T,core79TD
Note!1
The location of the cells placed using “placeInstsWithSites”
is not best location.
Please understand that this command considers power domain
but is just a function for placing cell on row. So be sure to check
the cell location.
row
row
row
Where is the best place?
?
LS
Disjoint row
“placeInstsWirhSites”
select this row, but….
?
Please review by the engineer

## Slide 49: 5V Level Shifter place (core79TD,core107)
5V Level Shifter place
core107T,core79TD
Note２！
NIMH.command.v4.1.etf have a bug.
If cpre107T and coe79TD are execute at the same time, cell overlap will occur.
In order to avoid this bug, core107T and core79TD place are executed separately.
placeInstsWithSites “core107T core79TD“ << NG!
placeInstsWithSites "core107T"
dbSet [dbGet top.insts.cell.site.name core107T -p3].pStatus fixed
placeInstsWithSites "core79TD"
dbSet [dbGet top.insts.cell.site.name core79TD -p3].pStatus fixed
Also, the DRV between the OBS in the cell and P/G mesh line is not considered during placement.
Currently, there is no choice but to fix it by hand.
Bug fixed command will be released soon.
executed separately

## Slide 50: Appendix
・Know-how to debug disjoined blockage coordinates
・Blockage Naming Rule for Row generation
・GuardRing Naming Rule
・GuardRing distance Rule

## Slide 51: Know-how to debug disjoined blockage coordinates
Next page introduces know-how and utilities to help you debug efficiently.
Efficiently aligning the coordinates of the disjoint rows is a very laborious task.
This is the rule.
INNOVUS requires alignment disjoint Rows.
This chapter will show you how to efficiently align blockage shape to the coordinates that fit the rules.
Check Blockage coordinate

## Slide 52: Know-how to debug disjoined blockage coordinates
Check alignment for core48T
Check alignment for core79TD
Check alignment for 107T
Command;
util_change_row_for_moving_const_box -site core48T
util_set_row_pd_island_for_u2c -job_type check_off_grid -site core48T
-> if no error, output blockage tcl file.
Command;
util_change_row_for_moving_const_box -site core79TD
util_set_row_pd_island_for_u2c -job_type check_off_grid -site core79TD
-> if no error, output blockage tcl file.
Command;
util_change_row_for_moving_const_box -site core107T
util_set_row_pd_island_for_u2c -job_type check_off_grid -site core107T
-> if no error, output blockage tcl file.
Debugging the blockage coordinates is done for each blockage.
For details, see the next page.
There is a check command if the disjoined blockage coordinates is not alignment.
source $COMMON_INNO/UTIL/util_set_row_pd_island_for_u2c.tcl
util_set_row_pd_island_for_u2c -job_type check_off_grid
Check Blockage coordinate

## Slide 53: Know-how to align disjoined blockage
1st step:
Set the following when creating a blockage.
Innovus > setFPlanMode -snapPlaceBlockageGrid inst
2nd step:
DEF output of CORE7T
The shape of core7T is created by Cut Row, so off-grid Row does not occur.
When debugging other ROWs, core7T ROW is deleted. so core7T is dumped
to DEF in advance.
Innovus > util_change_row_for_moving_const_box -save_org_row
Dump DEF file
Check Blockage coordinate

## Slide 54: Know-how to align disjoined blockage
3rd step: (case core48T)
In order to align the coordinates of each blockage of core48T,
fill whole chips with Row of core48T.
Innovus > util_change_row_for_moving_const_box -site core48T
> 5th step:
Check off-the-grid blockage.
You can check the misalignment blockage with the following command.
Innovus > util_set_row_pd_island_for_u2c -job_type check_off_grid -site core48T
Adjust the coordinates until there are no errors.
Fill with core48T
> 4th step:
work to fit each blockage to the grid.
Align the shape of the Core48T blockage to match the Row.
Align the blockage shapes.
Fit on grid
Fit on grid
Correct only the blockage for CORE48T.
Check Blockage coordinate

## Slide 55: Know-how to align disjoined blockage
6th Step:
If the error disappears in 5th step, output the blockage file of core48T.
Innovus > deselectAll
Innovus > select_obj [dbGet top.fplan.pBlkgs.name core47T* -p]
Innovus > writeFPlanScript -selected –filename modify_BK_4_create_row_box_fplan.tcl
Innovus > deselectAll
Dump blockage tcl
select
select
Blockage file for core48T
After debugging core48T, change the target to core79TD and core107T
and continue debugging.
Check Blockage coordinate

## Slide 56: Know-how to align disjoined blockage
7th Step:
Restore the core7T DEF output in step 2.
Dump DEF file
Innovus > setFPlanMode -snapPlaceBlockageGrid manufacturing
Innovus > util_change_row_for_moving_const_box -restore_org_row
Check Blockage coordinate

## Slide 57: Know-how to make blockage
Corresponding part in the 100_init.tcl
if {0} {
puts "suspend after PD area creation check"
setFPlanMode -snapPlaceBlockageGrid inst
util_change_row_for_moving_const_box -save_org_row
suspend
util_change_row_for_moving_const_box -site core48T
util_set_row_pd_island_for_u2c -job_type check_off_grid -site core48T
### save modified pBlk box(setting for PD and row) ###
deselectAll
select_obj [dbGet top.fplan.pBlkgs.name core48T* -p]
writeFPlanScript -selected -fileName modify_BK_4_create_48row_box_fplan.tcl
deselectAll
suspend
util_change_row_for_moving_const_box -site core79TD
util_set_row_pd_island_for_u2c -job_type check_off_grid -site core79TD
### save modified pBlk box(setting for PD and row) ###
deselectAll
select_obj [dbGet top.fplan.pBlkgs.name core79TD* -p]
writeFPlanScript -selected -fileName modify_BK_4_create_79row_box_fplan.tcl
deselectAll
suspend
util_change_row_for_moving_const_box -site core107T
util_set_row_pd_island_for_u2c -job_type check_off_grid -site core107T
### save modified pBlk box(setting for PD and row) ###
deselectAll
select_obj [dbGet top.fplan.pBlkgs.name core107* -p]
writeFPlanScript -selected -fileName modify_BK_4_create_107row_box_fplan.tcl
deselectAll
setFPlanMode -snapPlaceBlockageGrid manufacturing
util_change_row_for_moving_const_box -restore_org_row
}
#####
Check Blockage coordinate

## Slide 58: Know-how to make blockage
If the chip has multiple Rows, INNOVUS will align the blockage coordinates with the grid of nearby core rows.
CORE7T
PBK for Core48T
If you place a core48T blockage near core7T, the Core48T placement blockage
coordinates will be automatically snaped to the core7T placement grid.
X
X
Innovus is snaped to the core7T grid automatically.
X
When debugging Row coordinates, it is recommended to fill the target Row with the chip.
Fill CORE48T
PBK for Core48T
X
X
X
Align for core48T grid.
Check Blockage coordinate

## Slide 59: Blockage Naming Rule for Row generation
  Blockage Name format; Column1%Column2%Column3%Column4%Column5%Column6%Column7%Column8
  unit7T unit7T%Power_Domain_name%%%1V%woDNW%%<Suffix> Single Guard Ring
  unit7T unit7T%Power_Domain_name%%%1V%wDNW%%<Suffix> Double Guard Ring
  unit48T unit48T%Power_Domain_name%%%5V%woDNW%%<Suffix> Single Guard Ring
  unit48T unit48T%Power_Domain_name%%%5V%wDNW%%<Suffix> Double Guard Ring
  unit79TD unit79TD%Power_Domain_name%2nd_Power%2nd_Gnd%1V%woDNW%<DL>%<Suffix> Single Guard Ring
  unit107T unit107T%Power_Domain_name%2nd_Power%2nd_Gnd%5V%woDNW%<UL>%<Suffix> Single Guard Ring
  HardIP HardIP%Power_Domain_name%%%5V%woDNW%<IP>%<Suffix> Single Guard Ring
  SoftIP SoftIP%Power_Domain_name%%%1V%woDNW%<IP>%<Suffix> Single Guard Ring
  * If column1 is unit7T or unit48T , column3 and column4 can be omitted. The delimiter “%” cannot be omitted.
  Naming E.g. unit7T%PD_AWOVDD_VSS%%%1V%woDNW%%
  unit79TD%PD_OSCVCC_OSCVSS%AWOVDD%VSS%1V%woDNW%DL%
  HardIP%PD_AAVCC_AAVSS%%%5V%woDNW%ADA%

## Slide 60: GuardRing Naming Rule
  unit7T inst_guard_<Power_Domain_name>_1V_woDNW_<Suffix> FHFV1GRGV*
  unit7T inst_guard_<Power_Domain_name>_1V_wDNW_in_<Suffix> FHFV1GRGV*
  inst_guard_<Power_Domain_name>_1V_wDNW_out_<Suffix> ARV28OTR0005P10S*
  unit48 inst_guard_<Power_Domain_name>_5V_woDNW_<Suffix> FHFV5GRGV*
  unit48 inst_guard_<Power_Domain_name>_5V_wDNW_in_<Suffix> ARV28OTR0005NP9S*
  inst_guard_<Power_Domain_name>_5V_wDNW_out_<Suffix> ARV28OTR0005P10S*
  unit79TD inst_guard_<Power_Domain_name>_<2nd_Power>_<2nd_Gnd>_1V_woDNW_<DL>_<Suffix> FHFV1GRGV*
  unit107T inst_guard_<Power_Domain_name>_<2nd_Power>_<2nd_Gnd>_5V_woDNW_<UL>_<Suffix> FHFV5GRGV*
  HardIP inst_guard_<Power_Domain_name>_5V_woDNW_<IP>_<Suffix> ARV28OTR0005P10S*
  SoftIP inst_guard_<Power_Domain_name>_1V_woDNW_<IP>_<Suffix> FHFV1GRGV*
  IO inst_guard_IO_<Suffix>
  Name E.g. inst_guard_PD_AWOVDD_VSS_1V_woDNW_0001
  inst_guard_PD_OSCVCC_OSCVSS_AWOVDD_VSS_1V_woDNW_DL_0001
  inst_guard_PD_AAVCC_AAVSS_5V_woDNW_ADA_0001

## Slide 61: Blockage Naming Rule for Row generation
  Blockage Name format; Column1%Column2%Column3%Column4%Column5%Column6%Column7%Column8
  Column1;unitName [core7T / core48T / core79TD / core107T]
  Column2;PowerDomainName Match with the name defined in UPF
  Column3;2nd_Power Level shifter secondary power Name
  Column4;2nd_Gnd Level shifter secondary Ground Name
  Column5:Voltage [1V / 5V] Voltage of area shielded by guard ring
  Column6;Gurdring Line [woDNW / wDNW] ：Single Ring / Double Guard Ring
  Column7;LevelShifter Type [DL / UL / IP/ Non define ] : （Possible to omit）
  Column8;Suffix Suffix （Possible to omit）
Single Guard Ring
Double Guard Ring
Primary Power
1V or 5V ?
Unit Name
Power Domain name
Down
Shifter
Secondary
Ground
secondary
power
Primary
power
Primary
Ground
Up
Shifter
Secondary
Ground
secondary
power
Primary
power
Primary
Ground
How to judge?
See the next page.

## Slide 62: How to decide the guard ring type
Which one to choose?
Default Domain = PD_ISOVDD_VSS
PD_SYSVCC_VSS
=
Default Domain = PD_ISOVDD_VSS
PD_PLLVDD_PLLVSS
‡
Single Guard Ring
Double Guard Ring
Single Guard Ring
Double Guard Ring
Check the VSS name.
If the VSS name is the same as the default domain, a single guard ring is required.
If the VSS name is different from the default domain, a double guard ring is required.
?
Be sure to consult with the PV team as there are exceptions.

## Slide 63: Blockage Naming Rule for Row generation
  Blockage Name format; Column1%Column2%Column3%Column4%Column5%Column6%Column7%Column8
  unit7T core7T%Power_Domain_name%%%1V%woDNW%%<Suffix> Single Guard Ring
  unit7T core7T%Power_Domain_name%%%1V%wDNW%%<Suffix> Double Guard Ring
  unit48T core48T%Power_Domain_name%%%5V%woDNW%%<Suffix> Single Guard Ring
  unit48T core48T%Power_Domain_name%%%5V%wDNW%%<Suffix> Double Guard Ring
  unit79TD core79TD%Power_Domain_name%2nd_Power%2nd_Gnd%1V%woDNW%<DL>%<Suffix> Single Guard Ring
  unit107T core107T%Power_Domain_name%2nd_Power%2nd_Gnd%5V%woDNW%<UL>%<Suffix> Single Guard Ring
  HardIP HardIP%Power_Domain_name%%%5V%woDNW%<IP>%<Suffix> Single Guard Ring
  SoftIP SoftIP%Power_Domain_name%%%1V%woDNW%<IP>%<Suffix> Single Guard Ring
  * If column1 is unit7T or unit48T , column3 and column4 can be omitted. The delimiter “%” cannot be omitted.
  Naming E.g. core7T%PD_AWOVDD_VSS%%%1V%woDNW%%
  core79TD%PD_OSCVCC_OSCVSS%AWOVDD%VSS%1V%woDNW%DL%
  HardIP%PD_AAVCC_AAVSS%%%5V%woDNW%ADA%

## Slide 64: GuardRing Naming Rule
  unit7T inst_guard_<Power_Domain_name>_1V_woDNW_<Suffix> FHFV1GRGV*
  unit7T inst_guard_<Power_Domain_name>_1V_wDNW_in_<Suffix> FHFV1GRGV*
  inst_guard_<Power_Domain_name>_1V_wDNW_out_<Suffix> ARV28OTR0005P10S*
  unit48 inst_guard_<Power_Domain_name>_5V_woDNW_<Suffix> FHFV5GRGV*
  unit48 inst_guard_<Power_Domain_name>_5V_wDNW_in_<Suffix> ARV28OTR0005NP9S*
  inst_guard_<Power_Domain_name>_5V_wDNW_out_<Suffix> ARV28OTR0005P10S*
  unit79TD inst_guard_<Power_Domain_name>_<2nd_Power>_<2nd_Gnd>_1V_woDNW_<DL>_<Suffix> FHFV1GRGV*
  unit107T inst_guard_<Power_Domain_name>_<2nd_Power>_<2nd_Gnd>_5V_woDNW_<UL>_<Suffix> FHFV5GRGV*
  HardIP inst_guard_<Power_Domain_name>_5V_woDNW_<IP>_<Suffix> ARV28OTR0005P10S*
  SoftIP inst_guard_<Power_Domain_name>_1V_woDNW_<IP>_<Suffix> FHFV1GRGV*
  IO inst_guard_IO_<Suffix>
  Name E.g. inst_guard_PD_AWOVDD_VSS_1V_woDNW_0001
  inst_guard_PD_OSCVCC_OSCVSS_AWOVDD_VSS_1V_woDNW_DL_0001
  inst_guard_PD_AAVCC_AAVSS_5V_woDNW_ADA_0001

## Slide 65: ENDCap Cell Naming Rule
  unit7T (DefaultDomain)
  boundarycell_ENDCAP_<PowerDomain>_<SerialNumber>
  (e.g.) boundarycell_ENDCAP_PD_ISOVDD_VSS_88403
  (where CellType name is “BOUNDARY_RIGHTBWP7T40P140”)
  unit7T (Not DefaultDomain)
  <PowerDomainHierarchy>/boundarycell_ENDCAP_<PowerDomain>_<SerialNumber>
  (e.g.) MEM_TOP/awovdd_scdshold/boundarycell_ENDCAP_PD_AWOVDD_VSS_9210
  unit48T
  <PowerDomainHierarchy>/boundarycell_ENDCAP48 _<PowerDomain>_<SerialNumber>
  (e.g.) LVS_TOP/vcc33_LVS/boundarycell_ENDCAP48_PD_SYSVCC_VSS_1176
  unit79TD
  <PowerDomainHierarchy>/boundarycell_ENDCAP79_<2nd_Power>_to_<PowerDomain>_<SerialNumber>
  (e.g.) MEM_TOP/awovdd_scdshold/boundarycell_ENDCAP79_ SYSVCC_ to_PD_AWOVDD_VSS_92
  unit107T
  <PowerDomainHierarchy>/boundarycell_ENDCAP107_<2nd_Power>_to_<PowerDomain>_<SerialNumber>
  (e.g.) LVS_TOP/vcc33_LVS/ boundarycell_ENDCAP107_AWOVDD_to_PD_VCC_VSS_1

## Slide 66: WELLTAP Cell Naming Rule
  unit7T (DefaultDomain)
  tapfiller_WTAP_<CellTypeName>_<PowerDomain>_<SerialNumber>
  (e.g.) tapfiller_WTAP_TAPCELLBWP7T40P140_PD_ISOVDD_VSS_108164
  (where CellType name is “TAPCELLBWP7T40P140”)
  unit7T (Not DefaultDomain)
  <PowerDomainHierarchy>/tapfiller_WTAP_<CellTypeName>_<PowerDomain>_<SerialNumber>
  (e.g.) MEM_TOP/awovdd_scdshold/tapfiller_WTAP_TAPCELLBWP7T40P140_PD_AWOVDD_VSS_9210
  unit79TD
  <PowerDomainHierarchy>/tapfiller_WTAP79_<2nd_Power>_to_<PowerDomain>_<SerialNumber>
  (e.g.) MEM_TOP/awovdd_scdshold/tapfiller_WTAP79_SYSVCC_ to_PD_AWOVDD_VSS_1
  unit107T
  <PowerDomainHierarchy>/tapfiller_WTAP107_<2nd_Power>_to_<PowerDomain>_<SerialNumber>
  (e.g.) LVS_TOP/vcc33_LVS/ tapfiller_WTAP107_AWOVDD_to_PD_VCC_VSS_1

## Slide 67: fILLER/CAP Cell Naming Rule
  unit7T
  <PowerDomainHierarchy>/xofiller_FILL(CAP)_<SerialNumber>
  (e.g.) U_tb_wrap_3834/xofiller_FILL_5115
  (e.g.) U_tb_wrap_3834/xofiller_CAP_10544
  unit48T
  <PowerDomainHierarchy>/xofiller_FILL(CAP)48 _<SerialNumber>
  (e.g.) SYS_TOP/pllvdc_top/xofiller_FILL48_24
  (e.g.) SYS_TOP/pllvdc_top/xofiller_CAP48_41
  unit79TD
  <PowerDomainHierarchy>/xofiller_FILL79_<2nd_Power>_ to_<PowerDomain>_<SerialNumber>
  (e.g.) MEM_TOP/awovdd_scdshold/xofiller_FILL79_ SYSVCC_ to_PD_AWOVDD_VSS_92
  unit107T
  <PowerDomainHierarchy>/xofiller_FILL107_ <2nd_Power>_to_<PowerDomain>_<SerialNumber>
  (e.g.) SYS_TOP/pllvdc_top//xofiller_FILL107_AWOVDD_to_PD_VCC_VSS_1

## Slide 68: GuardRing distance Rule
>3um
NW
VDD/VCC
VSS
Cell used: FHFV1GRGV*
FHFV5GRGV*
Blockage
1V/5V area
Stdcell or RAM
frame
ISOVDD region of the chip
>3um
Stdcell or RAM
frame
NW

## Slide 69: GuardRing distance Rule
ISOVDD region of the chip
>3um
>3um
Stdcell or RAM
frame
NW
NW
VDD
VSS
  Cell used: FHFV1GRGV*/ ARV28OTR0005P10S*
Blockage
1V/5V area
Stdcell or RAM
frame
VSS

## Slide 70: GuardRing distance Rule
ISOVDD region of the chip
>5um
>3um
Stdcell or RAM
frame
NW
VSS
  Cell used: ARV28OTR0005P10S*
Blockage
HardIP area
VSS
HardIP frame

## Slide 71: GuardRing Rule DNW（1V）
>0.1um
AVDD
AVSS
Cell used:
ARV28OTR0005P10S*
AVDD/AVSS region of the chip
>3um
Stdcell or RAM
frame
NW
VSS
VSS
Cell used:
FHFV1GRGV*/FHFV1GRGVCORNER
FHFV1GRGV*
FHFV1GRGV*
FHFV1GRGV*
FHFV1GRGV*
FHFV1GRGVCORNER
ARV28OTR0005P10S*
ARV28OTR0005P10S*
ARV28OTR0005P10S*
ARV28OTR0005P10S*

## Slide 72
Renesas.com